## Slide 1
Recovery modelling needs to be improved to better understand system’s resilience
Physics-based and modular computational workflow based on existing regional risk assessment tools used to assess resilience
Interdependencies among systems/components captured by simulating flow of resources and looking at resource demand fulfillment
iRe-CoDeS framework applied to housing and interdependent infrastructure to simulate recovery and assess disaster resilience

## Slide 3
Hazard module
Vulnerability module
Recovery module
Resilience quantification
module
Disaster intensity measure predictions
Regional damage/loss model
iRe-CoDeS recovery model
Re-CoDeS resilience assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.
Community properties
Soil type, terrain elevation, fault location, etc.
Exposure, fragility/vulnerability functions, etc.
Repair time, impeding factors, recovery resource supply, etc.
Community resilience goals
Blagojević, Kipfer, Didier, Stojadinović (2020) Probability-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.
Motivation
Resilience Assessment

## Slide 6
pyrecodes
pyrecodes
pyrecodes

## Slide 7: OLD SLIDES

## Slide 8: What is resilience?
Disruption
Time
Functionality
Resilient
Not so resilient

## Slide 9: How to assess the resilience of a system?
https://www.pinterest.ch/

## Slide 10: iRe-CoDeS framework: Discretize the system into components
Blagojević, Hefti, Henken, Didier, Stojadinović (2022) Quantifying Disaster Resilience of a Community with Interdependent Civil Infrastructure Systems. Structure and Infrastructure Engineering.

## Slide 11: Monitor/simulate components‘ resource supply and demand during recovery
Supply
Demand
Supply
Demand
Supply
Demand
Supply
Demand
Supply
Demand
Supply
Demand
Supply
Demand
Supply
Demand
Supply
Demand
Blagojević, Hefti, Henken, Didier, Stojadinović (2022) Quantifying Disaster Resilience of a Community with Interdependent Civil Infrastructure Systems. Structure and Infrastructure Engineering.

## Slide 12: Component‘s post-disaster performance
Repair Rate
Supply
Demand
Blagojević, Hefti, Henken, Didier, Stojadinović (2022) Quantifying Disaster Resilience of a Community with Interdependent Civil Infrastructure Systems. Structure and Infrastructure Engineering.
Damage Level
Time
Initial Damage level
Time
Component
Component‘s post-disaster supply/demand dynamics characterized using two parameters:
Initial Damage Level – from 0 (no damage) to 1 (complete damage)
Repair Rate – from 0 (no repair) to 1 (complete repair within one time step)

## Slide 13: Component interdependencies simulated as a flow of resources and services
Blagojević, Hefti, Henken, Didier, Stojadinović (2022) Quantifying Disaster Resilience of a Community with Interdependent Civil Infrastructure Systems. Structure and Infrastructure Engineering.
Resource distribution models

## Slide 14: Component interdependencies simulated as a flow of resources and services
Blagojević, Hefti, Henken, Didier, Stojadinović (2022) Quantifying Disaster Resilience of a Community with Interdependent Civil Infrastructure Systems. Structure and Infrastructure Engineering.
Resource distribution models

## Slide 15: Resilience assessment using system’s supply/demand/consumption
Post-disaster demand, supply and consumption of a system during recovery.
Didier, Broccardo, Esposito, Stojadinović (2018) A compositional demand/supply framework to quantify the resilience of civil infrastructure systems (Re-CoDeS). Sustainable and Resilient Infrastructure.
Disaster Resilience Quantification:
  System Supply:

## Slide 16: Resilience assessment using system’s supply/demand/consumption
Disaster Resilience Quantification:
  System Supply:
  System Demand:
Post-disaster demand, supply and consumption of a system during recovery.
Didier, Broccardo, Esposito, Stojadinović (2018) A compositional demand/supply framework to quantify the resilience of civil infrastructure systems (Re-CoDeS). Sustainable and Resilient Infrastructure.

## Slide 17: Resilience assessment using system’s supply/demand/consumption
Disaster Resilience Quantification:
  System Supply:
  System Demand:
  System Consumption:
Post-disaster demand, supply and consumption of a system during recovery.
Didier, Broccardo, Esposito, Stojadinović (2018) A compositional demand/supply framework to quantify the resilience of civil infrastructure systems (Re-CoDeS). Sustainable and Resilient Infrastructure.

## Slide 18: iRe-CoDeS and NIST Community Resilience Goals
Post-disaster demand, supply and consumption of a system during recovery.
Unmet demand
Desired percent of met demand
Time
Functionality
Disruption
Desired Functionality Level
Time to meet the target functionality level
Time to meet the goal
Blagojević, Didier, Stojadinović (2022) Evaluating NIST Community Disaster Resilience Goals using the iRe-CoDeS Resilience Quantification Framework. 12NCEE, Salt Lake City, USA.

## Slide 19: How to assess the resilience of a system? + Resilience is often assessed using models that consist of numerous interdependent components and whose performance needs to be understood + getting component data required a lot of effort , and is not possible in some cases due to privacy and security concerns + but some components might be irrelevant for assessing resilience, can we figure out which components those are before we collect data about them? + use sobol indices to rank components using uninformed input distributions + then iteratice heuristic upper and lower bound search to figure out what is irrelevant or what is the span of the distributions if no data available for some components + virtual community whose resilience goals are assessed illustrates the approach + explain iRe-CoDeS – supply/demand, interaction, initial damage level (0 to 1), repair rate (0 to 1)
https://www.pinterest.ch/

## Slide 20: Method for Component Importance Quantification - Step 1
Blagojevic, Didier, Stojadinovic (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety

## Slide 21: Method for Component Importance Quantification - Step 2
Blagojevic, Didier, Stojadinovic (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety

## Slide 22: Method for Component Importance Quantification - Step 3
Blagojevic, Didier, Stojadinovic (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety
Iteration 1
Iteration 2
Iteration 3

## Slide 23: iRe-CoDeS community resilience quantification and the Sobol’ method
Blagojevic, Didier, Stojadinovic (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety
Iteration 1
Iteration 2
Iteration 3

## Slide 24: Case Study: Virtual Community with interdependent infrastructure
Motivation
Resilience Assessment

## Slide 25: Case Study: Scenario Earthquake
Spatial distribution of the PGA for the considered scenario earthquake - hazard module output
Initial damage state of the virtual community due to the scenario earthquake (t=0) – vulnerability module output
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.
Hazard module
Vulnerability module
Motivation
Resilience Assessment

## Slide 26: Case Study: Assessing infastructure resilience to a scenario earthquake
Recovery of electric power supply without considering electric power plants’ dependance on other systems
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 27: Case Study: Assessing infastructure resilience to a scenario earthquake
Post-disaster change in electric power demand as people leave and return to buildings
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 28: Case Study: Assessing infastructure resilience to a scenario earthquake
Recovery of electric power consumption
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 29: Resilience assessment using system’s supply/demand/consumption
Post-disaster demand, supply and consumption of a system during recovery.
Disaster Resilience Quantification:
  System Supply:
  System Demand:
  System Consumption:
  Resilience Metric:
Didier, Broccardo, Esposito, Stojadinović (2018) A compositional demand/supply framework to quantify the resilience of civil infrastructure systems (Re-CoDeS). Sustainable and Resilient Infrastructure.

## Slide 30: Case Study: Assessing infastructure resilience to a scenario earthquake
Total unmet demand (LoR) for electric power over the recovery period is 649.2MWh without considering system interdependencies.
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 31: Case Study: Assessing infastructure resilience to a scenario earthquake
Recovery of electric power supply considering electric power plants’ dependance on cooling water and communication services.
Reduction in electric power supply during first 9 post-disaster days due to interdependency effects
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 32: Case Study: Assessing infastructure resilience to a scenario earthquake
Reduction in electric power consumption during first 9 post-disaster days due to interdependency effects
Recovery of electric power consumption considering electric power plants’ dependance on cooling water and communication services.
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 33: Case Study: Assessing infastructure resilience to a scenario earthquake
Total unmet demand (LoR) for electric power over the recovery period is 882.1MWh considering system interdependencies.
Motivation
Resilience Assessment
Blagojević, Kipfer, Didier, Stojadinović (2020) Scenario-based Resilience Assessment of Communities with Interdependent Civil Infrastructure Systems. Proceeding of the 17th World Conference on Earthquake Engineering. Sendai, Japan.

## Slide 34: Case Study: Assessing housing resilience to a scenario earthquake
Blagojević, Lauber, Didier, Stojadinović (2022) Evaluating the Importance of Interdependent Civil Infrastructure System Components for Disaster Resilience of Community Housing. Lifelines 2022, Los Angeles, USA.
Housing resilience assessment consistent with infrastructure resilience assessment: simulate housing supply/demand/consumption over the recovery period.
Motivation
Resilience Assessment

## Slide 35: Resilience Assessment of the Built Environment Recovery modelling in iRe-CoDeS

## Slide 36: How resilient do we need to be? Defining the desired community performance
NIST (2016) Community Resilience Planning Guide for Buildings and Infrastructure Systems. NIST Special Publication 1190.
Time
Functionality
Disruption
Desired Functionality Level
Time to meet the target functionality level
Motivation
Resilience Assessment

## Slide 37: Resilience assessment using system’s supply/demand/consumption
Post-disaster demand, supply and consumption of a system during recovery.
Disaster Resilience Quantification:
  System Supply:
  System Demand:
  System Consumption:
  Resilience Metric:
Didier, Broccardo, Esposito, Stojadinović (2018) A compositional demand/supply framework to quantify the resilience of civil infrastructure systems (Re-CoDeS). Sustainable and Resilient Infrastructure.
Motivation
Resilience Assessment

## Slide 38: iRe-CoDeS community resilience quantification and the Sobol’ method
Blagojević, Didier, Stojadinović (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety.
The importance of each component’s initial damage level and repair rate is quantified:
Repair Rate
Initial Damage Level
Repair Rate
Initial Damage Level
Repair Rate
Initial Damage Level
Component 1
Component 2
Component i
iRe-CoDeS community model
LoRR/S1
LoRR/Sn
Sobol’ method
INPUTS
OUTPUTS
COMPUTATIONAL MODEL
Motivation
Resilience Assessment
Resilience Improvement

## Slide 39: iRe-CoDeS community resilience quantification and the Sobol’ method
Input probability distributions are assumed with no information on components’ vulnerability and recoverability.
Repair Rate
Initial Damage Level
Repair Rate
Initial Damage Level
Repair Rate
Initial Damage Level
Component 1
Component 2
Component i
iRe-CoDeS community model
LoRR/S1
LoRR/Sn
Sobol’ method
INPUTS
OUTPUTS
COMPUTATIONAL MODEL
0
1
Probability
Motivation
Resilience Assessment
Resilience Improvement
Blagojević, Didier, Stojadinović (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety.

## Slide 40: Component Importance for the Electric Power System Resilience
Motivation
Resilience Assessment
Resilience Improvement

## Slide 41: Component Importance for the Communication System Resilience
Blagojević, Didier, Stojadinović (2022) Quantifying Component Importance for Disaster Resilience of Communities with Interdependent Civil Infrastructure Systems. Reliability Engineering and System Safety.
Probability distributions of the time to meet 90% of demand for communication service without any information on vulnerability and recoverability on half of community components.
Blagojević, Didier, Stojadinović (2023) Identifying Components Important for System Resilience. ICASP14’, Dublin, Ireland.
Motivation
Resilience Assessment
Resilience Improvement

## Slide 42: Conclusion

## Slide 43: Conclusion
iRe-CoDeS framework provides a foundation for simulating regional recovery and assessing built environment’s resilience:
Bottom-up framework – the effect of building-level interventions on community resilience can be investigated.

## Slide 44: Conclusion
iRe-CoDeS framework provides a foundation for simulating regional recovery and assessing built environment’s resilience:
Bottom-up framework – the effect of building-level interventions on community resilience can be investigated.
Component interaction simulated as a flow of resources – uses existing data on supply/demand and flow models.

## Slide 45: Conclusion
iRe-CoDeS framework provides a foundation for simulating regional recovery and assessing built environment’s resilience:
Bottom-up framework – the effect of building-level interventions on community resilience can be investigated.
Component interaction simulated as a flow of resources – uses existing data on supply/demand and flow models.
Extensible and modular – third-party models can be integrated within the framework.

## Slide 46: Conclusion
iRe-CoDeS framework provides a foundation for simulating regional recovery and assessing built environment’s resilience:
Bottom-up framework – the effect of building-level interventions on community resilience can be investigated.
Component interaction simulated as a flow of resources – uses existing data on supply/demand and flow models.
Extensible and modular – third-party models can be integrated within the framework.
Can be used for probabilistic assessment of community resilience goals.

## Slide 47: Conclusion
iRe-CoDeS framework provides a foundation for simulating regional recovery and assessing built environment’s resilience:
Bottom-up framework – the effect of building-level interventions on community resilience can be investigated.
Component interaction simulated as a flow of resources – uses existing data on supply/demand and flow models.
Extensible and modular – third-party models can be integrated within the framework.
Can be used for probabilistic assessment of community resilience goals.
Consistent across various subsystems of the built environment.
Electric Power
Housing
Recovery Resources

## Slide 48: Conclusion
iRe-CoDeS framework provides a foundation for simulating regional recovery and assessing built environment’s resilience:
Bottom-up framework – the effect of building-level interventions on community resilience can be investigated.
Component interaction simulated as a flow of resources – uses existing data on supply/demand and flow models.
Extensible and modular – third-party models can be integrated within the framework.
Can be used for probabilistic assessment of community resilience goals.
Consistent across various subsystems of the built environment.
Continuous resilience-based design of the built environment possible with the iRe-CoDeS framework.